## Slide 1: NETWORK PERFORMANCE ANALYSIS
Batch-2
Reg.No:211FA04064
211FA04139
211FA04426
211FA04563

## Slide 2: PROBLEM STATEMENT:
a. Describe the most popular wireless Internet access technologies today. Compare and contrast them.
EXTENSION:
Imagine future scenarios where wireless technologies seamlessly integrate into daily life and propose potential benefits and challenges.

## Slide 3
Wi-Fi (802.11x):
Popularity: Ubiquitous, found in homes, businesses, public spaces.
Range: Typically limited to a few hundred feet from the access point.
Speed: Offers high-speed connections, with newer standards (such as Wi-Fi 6) providing faster data rates.
Deployment: Requires access points for connectivity.
Security: Supports various encryption protocols like WPA3, ensuring secure connections.
Use Case: Ideal for indoor use in homes, offices, cafes, etc.
4G LTE (Long Term Evolution):
Popularity: Widely used for mobile Internet access.
Range: Can cover large geographic areas, depending on the network infrastructure.
Speed: Provides high-speed data access, suitable for streaming, browsing, etc.
Deployment: Requires cellular towers and network infrastructure.
Security: Utilizes encryption for secure data transmission.
Use Case: Primary mode of Internet access for smartphones and mobile devices.

## Slide 4
Satellite Internet:
Popularity: Commonly used in rural and remote areas with limited terrestrial infrastructure.
Range: Provides coverage over wide geographic areas, including remote regions.
Speed: Generally slower and more prone to latency due to the longer distance data must travel.
Deployment: Requires satellite dish installation.
Security: Encryption protocols are used to secure data transmission.
Use Case: Ideal for areas where terrestrial Internet options are limited or unavailable.
Fixed Wireless Access (FWA):
Popularity: Used as an alternative to wired broadband in some areas.
Range: Can cover moderate distances, often used in suburban or rural areas.
Speed: Offers broadband speeds comparable to DSL or cable.
Deployment: Utilizes fixed wireless towers to provide connectivity to homes and businesses.
Security: Similar to Wi-Fi, employs encryption standards for secure connections.
Use Case: Provides broadband Internet access where laying cables is impractical or costly.

## Slide 5: EXTENSION:
Benefits:
1.Enhanced Connectivity: With ubiquitous wireless coverage, people will be able to stay connected wherever they go, facilitating communication, access to information, and collaboration.
2.IoT Integration: Wireless connectivity will enable the proliferation of Internet of Things (IoT) devices, leading to smart homes, cities, and workplaces. This can result in improved efficiency, resource management, and convenience.
3.Mobility: Wireless technologies will enable greater mobility, allowing people to work, shop, and interact while on the move. This can lead to increased productivity and flexibility in daily routines.
4.Innovation: Seamless wireless connectivity will foster innovation in various sectors, including healthcare, transportation, entertainment, and education. New applications and services will emerge, improving quality of life and creating economic opportunities.
5.Accessibility: Wireless technologies can bridge the digital divide by providing access to the Internet and digital services in underserved areas. This can democratize information and empower marginalized communities.

## Slide 6
Challenges:
1.Privacy and Security: With increased connectivity comes greater risks of privacy breaches, cyberattacks, and surveillance. Protecting sensitive data and ensuring cybersecurity will become more challenging.
2.Infrastructure Requirements: Deploying and maintaining wireless infrastructure, such as 5G networks and IoT sensors, will require significant investments in equipment, spectrum, and regulatory frameworks. Ensuring equitable access to infrastructure may pose logistical and financial challenges.
3.Spectrum Congestion: As the number of wireless devices grows, spectrum congestion may become a bottleneck, leading to slower speeds, dropped connections, and degraded service quality. Efficient spectrum management and technological innovations will be necessary to address this issue.
4.Health Concerns: The long-term health effects of prolonged exposure to wireless radiation are still not fully understood. Public concerns about electromagnetic radiation and its potential impact on human health may arise, necessitating ongoing research and risk mitigation measures.
5.Digital Divide: While wireless technologies have the potential to bridge the digital divide, disparities in access, affordability, and digital literacy may persist. Ensuring equitable access to wireless connectivity and addressing socioeconomic barriers will be essential for inclusive development.

## Slide 7: PROBLEM STATEMENT:
b. Consider sending a packet from a source host to a destination host over a fixed route. List the delay components in the end-to-end delay. Which of these delays are constant and which are variable?

## Slide 8
1.Propagation Delay: This is the time it takes for a signal to travel from the source to the destination. It depends on the distance between the source and destination and the speed of propagation through the medium (typically the speed of light in fiber optic cables or radio waves in wireless communication). Propagation delay is generally constant for a given distance and medium.
2.Transmission Delay: This is the time it takes to push all of the packet's bits into the link. It depends on the packet's size (in bits) and the transmission rate (in bits per second) of the link. Transmission delay is constant for a given packet size and link transmission rate.
3.Queueing Delay: This occurs when the packet must wait in a queue at a router or switch before it can be transmitted. It depends on the level of congestion in the network and the scheduling algorithms used by routers. Queueing delay is variable and can fluctuate based on network conditions.
4.Processing Delay: This is the time it takes for the routers or switches to examine the packet's header and make forwarding decisions. It depends on the processing capabilities of the router or switch and the complexity of the forwarding logic. Processing delay is generally constant for a given router or switch configuration.

## Slide 9: PROBLEM STATEMENT:
C. Suppose Host A wants to send a large file to Host B. The path from Host A to Host B has three links, of rates R1 = 500 kbps, R2 = 2 Mbps, and R3 = 1 Mbps.
i. Assuming no other traffic in the network, what is the throughput for the file transfer?
ii. Suppose the file is 4 million bytes. Dividing the file size by the throughput, roughly how long will it take to transfer the file to Host B?
EXTENSION:
Extension:- R3 upgraded to 2 Mbps; R3 upgraded to 3 Mbps;R3 upgraded to 10 Mbps.

## Slide 10
C)
File Transfer Over Three Links:
Throughput Calculation:-
Assuming no other traffic, the throughput is limited by the link with the lowest rate.-
Throughput (T) = Minimum(R1, R2, R3) = 500kbps
ii. File Transfer Time Calculation:-
- File Size = 4 million bytes.
- File Transfer Time (T transfer ) = File Size / Throughput.
- transfer=4 MB×8 bits/byte/500 kbps
- T transfer≈64 seconds.

## Slide 11: EXTENSION:
CLIENTSERVER:-
package Networking;
import java.io.*;
import java.net.Socket;
import java.util.Scanner;
import java.net.DatagramPacket;
import java.net.DatagramSocket;
public class ClientServer {
public static void main(String[] args) {
try {
DatagramSocket datagramSocket = new DatagramSocket(8888);
byte[] datagramBuffer = new byte[1024];
DatagramPacket packet = new DatagramPacket(datagramBuffer, datagramBuffer.length);
datagramSocket.receive(packet);
String broadcastMessage = new String(packet.getData(), 0, packet.getLength());
System.out.println("Received message: " + broadcastMessage);
if (broadcastMessage.equals("SERVER_IP_BROADCAST"))
")) {
String serverIP = packet.getAddress().getHostAddress();
System.out.println("Server IP is: " + serverIP); Scanner scanner = new Scanner(System.in);
while (true) {
Socket socket = new Socket(serverIP, 900);
try (socket; DataOutputStream dataOutputStream = new DataOutputStream(socket.getOutputStream())) {
System.out.println("Enter the type of data you want to send (text/file):");
String dataType = scanner.nextLine();
dataOutputStream.writeUTF(dataType);
switch (dataType) {
case "text" -> {
System.out.println("Enter the text message:");
String message = scanner.nextLine();
dataOutputStream.writeUTF(message);
double transmissionDelayText = calculateTransmissionDelay(message.getBytes().length, 300);
System.out.println("Transmission Delay for text: " + transmissionDelayText + " seconds");
}
case "file" -> {
System.out.println("Enter the file path:");
String filePath = scanner.nextLine();
File file = new File(filePath);
long fileSize = file.length(); dataOutputStream.writeLong(fileSize);
FileInputStream fileInputStream = new FileInputStream(file);
byte[] buffer = new byte[4 * 1024];
int bytes;
long totalBytesSent = 0;

## Slide 12
long startTime = System.currentTimeMillis();
Thread.sleep(1);
double speed = 0;
while ((bytes = fileInputStream.read(buffer)) != -1) {
dataOutputStream.write(buffer, 0, bytes);
totalBytesSent += bytes;
long currentTime = System.currentTimeMillis();
speed = (double) totalBytesSent / ((currentTime - startTime) / 1000.0);
System.out.print("-");
double transmissionDelayChunk = calculateTransmissionDelay(bytes, 300);
System.out.println("Transmission Delay for this chunk: " + transmissionDelayChunk + " seconds");
}
long endTime = System.currentTimeMillis();
double transmissionRate = (double) totalBytesSent / ((endTime - startTime) / 1000.0);
System.out.println("\nFile sent at speed: " + speed + " bytes/s");
System.out.println("Transmission rate: " + transmissionRate + " bytes/s");
double transmissionDelayFile = calculateTransmissionDelay(fileSize, 300);
System.out.println("Transmission Delay for file: " + transmissionDelayFile + "ms");
fileInputStream.close();
}
default -> System.out.println("Unknown data type. Please enter 'text' or 'file'.");
}
} catch (IOException e) {
System.out.println("Error sending data. Attempting to reconnect...");
e.fillInStackTrace();
}
}
}
datagramSocket.close();
} catch (Exception e) {
System.out.println("Error connecting to server");
e.fillInStackTrace();
}
}
public static double calculateTransmissionDelay(double packetSizeBytes, double linkSpeedMbps) {
double linkSpeedBps = linkSpeedMbps *
1_000_000;
double packetizationDelaySeconds = packetSizeBytes * 8 / linkSpeedBps;
double serializationDelaySeconds = packetSizeBytes * 8 / linkSpeedBps;
return packetizationDelaySeconds + serializationDelaySeconds;
}
}
package Networking;
public class TransmissionDelay {
// Assuming packet size in bytes and link speed in Mbps

## Slide 13
public static double calculateTransmissionDelay(double packetSizeBytes, double linkSpeedMbps) {
// Convert link speed to bits per second
double linkSpeedBps = linkSpeedMbps * 1_000_000;
// Packetization Delay: Calculate the time to packetize the data
double packetizationDelaySeconds = packetSizeBytes * 8 / linkSpeedBps;
// Serialization Delay: Calculate the time to transmit each packet over the link
double serializationDelaySeconds = packetSizeBytes * 8 / linkSpeedBps;
// Aggregate Delay: Sum of Packetization Delay and Serialization Delay
double transmissionDelaySeconds = packetizationDelaySeconds + serializationDelaySeconds;
return transmissionDelaySeconds;
}
public static void main(String[] args) {
// Example usage
double packetSizeBytes = 1500; // Typical packet size in bytes
double linkSpeedMbps = 300; // Aggregated link speed in Mbps
double transmissionDelaySeconds = calculateTransmissionDelay(packetSizeBytes,
linkSpeedMbps);
System.out.println("Transmission Delay: " + transmissionDelaySeconds + " seconds");
}
}
package Networking;
import java.io.DataInputStream;
import java.io.DataOutputStream;
import java.io.FileOutputStream;
import java.io.IOException;
import java.net.*;
public class ServerThreads {
public static void main(String[] args)
{
new Thread(() -> {
try {
DatagramSocket socket = new DatagramSocket();
String message = "SERVER_IP_BROADCAST";
DatagramPacket packet = new DatagramPacket(message.getBytes(), message.getBytes().length, InetAddress.getByName("255.255.255.255"), 8888);
while (true) {
socket.send(packet);
// System.out.println("Broadcast message sent"); // print statement
try {
Thread.sleep(5000); // sleep for 5 seconds before sending the next broadcast
} catch (InterruptedException e) {
e.fillInStackTrace();
}
}
} catch (IOException e) {
e.fillInStackTrace();
}
}).start();

## Slide 14
try (ServerSocket serverSocket = new ServerSocket(900)) {
System.out.println("Server is Starting in Port 900");
while (true) {
// Accept the Client request using accept method
Socket clientSocket = serverSocket.accept();
System.out.println("Connected");
// Create a new thread for each client
new Thread(() -> {
try {
handleClient(clientSocket);
} catch (Exception e) {
e.fillInStackTrace();
}
}).start();
}
}
catch (Exception e) {
e.fillInStackTrace();
}
}
private static void handleClient(Socket clientSocket) {
try {
DataInputStream dataInputStream = new DataInputStream(clientSocket.getInputStream());
DataOutputStream dataOutputStream = new DataOutputStream(clientSocket.getOutputStream());
String dataType = dataInputStream.readUTF(); // read data
type from client
switch (dataType) {
case "text" -> {
String message = dataInputStream.readUTF();
System.out.println("Received message: " + message + " from " + clientSocket.getRemoteSocketAddress()); }
case "file" -> {
// save file name with ip address like ''192.168.0.105_received_file.pdf''
String fileName = clientSocket.getRemoteSocketAddress().toString().replace("/", "").replace(":", "_") + "_received_file.pdf";
receiveFile(fileName, dataInputStream); // read file from client
}
// Add more cases here to handle other types of data
default ->
System.out.println("Unknown data type received from " + clientSocket.getRemoteSocketAddress());
}
dataInputStream.close();
dataOutputStream.close();
clientSocket.close();
} catch (IOException e) {
System.out.println("Error handling client " + clientSocket.getRemoteSocketAddress());
e.fillInStackTrace();
} catch (Exception e) {
throw new RuntimeException(e);
}
}
// receive file function is start here
private static void receiveFile(String fileName, DataInputStream dataInputStream)

## Slide 15
throws Exception
{
int bytes = 0;
long totalBytesReceived = 0;
System.out.println("Start time: " + startTime);
while (size > 0 && (bytes = dataInputStream.read(buffer, 0, (int)Math.min(buffer.length, size))) != -1) {
// Here we write the file using write method
fileOutputStream.write(buffer, 0, bytes);
size -= bytes; // read upto file size
totalBytesReceived += bytes;
}
long endTime = System.currentTimeMillis();
// Print the ending time
System.out.println("End time: " + endTime);
// Here we received file
System.out.println("File is Received");
long delay = endTime - startTime;
long loss = size; // Corrected here
double throughput = (double) totalBytesReceived / delay;
System.out.println("Delay: " + delay + " ms");
System.out.println("Loss: " + loss + " bytes");
System.out.println("Throughput: " + throughput + " bytes/ms");
fileOutputStream.close();
}
}